## Slide 1
Digital Electronic Circuits Section 1 (EE, IE)
Lecture 1

## Slide 2
Why Digital?
- Digital Clock, Digital Camera, Digital Money, Digital Media, …
Popular terms of current times:
Prefix ‘Digital’ associates a term with digital technology.
Digital technology is considered more efficient for reasons such as:
- Easy to store, copy, compress - Immunity: noise, interference
- Various transmission options - Error correction, encryption
- Flexibility in processing - Analysis of data
- Inexpensive building block

## Slide 3
What is Digital?
Digital signals represent only finite number of discreet values (2 valued: Binary).
- Signal is discreet by nature - Signal, analog by nature, converted to discreet
Digital systems represent and manipulate digital signals.

## Slide 4
Manipulation of Digital Signals
Switching is key to manipulation of digital signals.
Digital data storage involves switching.

## Slide 5
Switching & Logic Operation
Realization of AND

## Slide 6
Switching & Logic Operation
Realization of OR

## Slide 7
Switching & Logic Operation
Realization of NOT

## Slide 8
Switching Circuits
Realization of Tristate

## Slide 9
Diode as a switch
Realization of AND, OR logic
Possibility of realizing NOT logic

## Slide 10
Transistor as a switch
Realization of NOT gate (inverter), Input-Output Characteristics
Vin
Vout
VOH
VOL
VIH
VIL
1 2 3 4 5
1
2
3
4
5
(in Volt)
(in Volt)
Cut-off
Active
Saturation
For quantitative analysis:
RB = 10 kΩ
RC = 1 kΩ
βF = 50
VBE(ON) = VBE(Sat) = 0.7V
VCE(Sat) = 0.2V

## Slide 11
Transistor as a switch
Cut-off region
Base current IB = 0 till VBE < 0.7V i.e. Vin < 0.7V.
Transistor is cut off and IC = 0 with Vout = 5V over entire range.
When Vin is increased beyond 0.7V, base current begins to flow and the transistor moves from cut off region to normal active region.
The coordinate, Vin = 0.7V, Vout = 5V mark first transition point in the transfer function of this circuit. This is also termed as breakpoint or edge of cutoff (EOC).
EOC

## Slide 12
Transistor as a switch
Active region
Applying KVL along Vin, RB, VBE, Ground
IB = (Vin – VBE(on))/RB
In active region, IC = F IB (as long as VCE < VCE(sat))
Applying KVL along Vcc, RC, VCE, Ground
Vout = VCC - IC RC = VCC - F IB RC
Combining,
Vout = VCC - F RC (Vin – VBE(on))/RB

## Slide 13
Transistor as a switch
Saturation region
As Vin (or IB) is increased a second transition point is reached when Vout = VCE(sat).
The values of IC and IB for this condition (the subscript EOS means edge of saturation):
IC(EOS) = (VCC – VCE(sat))/RC = (5-0.2)/1 = 4.8mA
and IB(EOS) = IC(EOS)/F = 4.8/50 = 0.096mA
Then Vin(EOS) = VBE(on) + IB(EOS) RB = 0.7 + (0.096)(10) = 1.66V
Thus Vin  1.66V the transistor saturates. (Saturating Logic)
EOS

## Slide 14
Input-Output Mapping
Noise Margin, Transition width and Logic swing
NML = VIL – VOL = 0.7 – 0.2 = 0.5V
NMH = VOH – VIH = 5.0 – 1.66 = 3.34V
Transition width = VIH - VIL
= 1.66 – 0.7 = 0.96V
Logic swing = VOH - VOL
= 5 – 0.2 = 4.8V
NMH
NML
T.W.
L.S.

## Slide 15
Fanout
When Vin is HIGH, driver transistor is saturated and Vout will be LOW.
With VCE(sat) = 0.2V all the load gates will be in the OFF state.
No restriction on number of load gates
Input to driver transistor: HIGH

## Slide 16
Fanout
When Vin is LOW, driver transistor will be OFF and Vout will be at HIGH level.
A limit in the fanout is set when the voltage at Vout is insufficient to saturate load gate transistors.
Note that VIH = 1.66V
For driver, IC(driver) = (VCC – Vout)/RC = (5 – 1.66)/1 = 3.34 mA
For load, IB(load) = (Vout – VBE(sat))/RB
= (1.66 – 0.7)/10 = 0.096 mA
N = IC(driver)/IB(load) = 34.79  34
Input to driver transistor: LOW

## Slide 17
Fanout
Effect of noise margin
For a 0.5V noise margin,
Minimum HIGH level voltage at Vout
VOH = VIH + NMH = 1.66 + 0.5 = 2.16V
Similar calculation as before with Vout at 2.16V gives
IC(driver) = (VCC – Vout)/RC = (5 – 2.16)/1 = 2.84 mA
IB(load) = (Vout – VBE(sat))/RB = (2.16 – 0.7)/10 = 0.15 mA
N = IC(driver)/IB(load) = 19.4  19
An increased NMH reduces fanout even further
Other factors:
Variation in F, VBE(sat), VCE(sat), VCC, RC, RB.

## Slide 18
References:
Grinich, V.H., and H.G. Jackson, Introduction to Integrated Circuits, McGraw-Hill
Donald P. Leach, Albert P. Malvino and Goutam Saha, Digital Principles & Applications 8e, McGraw Hill
Herbert Taub, and Donald Schilling, Digital Integrated Electronics, McGraw Hill
M. Morris Mano, and Michael D. Ciletti, Digital Design 5e, Pearson

## Slide 19: https://tinyurl.com/DEC2020-Sec1-Quiz1
Time: 10 minutes